## Slide 1: 1-Color IR Wavelengths for Specific Temperature Measurement Applications Lowest Starting Temperature Measurement Range
8-14 µm General Purpose – Dull Surface Materials………………… -40°C/-40°F
7.9 µm Plastic Films & Ultra Thin Glass…………….. 0°C/32 °F
3.43 µm Plastic Film (polypropylene, polystyrene, polyethylene)…………… 50°C/122 °F
5 µm Glass (surface)………………. 100°C/212 °F
4.5 /4.6 µm C02 Gas and Flames……………………. 100°C/212 °F
3.9 µm See through Clean Flames & Hot Combustible Gases…………… 200°C/392 °F
2.0-2.8 µm Low Temperature Metals, Reflective Materials ………………………. 50°C/122 °F
0.78-1.8 µm Metals, Reflective Materials, (Molten Glass / Semiconductor wafer @1u) … 550°C/1022 °F
0.65 µm Very Hot Applications …………… 900°C /1652°F